## Slide 1: What’s New in SigmaXL® Version 11 Part 3 of 3: Evaluating Response Surface Designs with the Fraction of Design Space (FDS) Plot and Introduction to Optimal Designs July 30, 2025
John Noguera, P.Eng. CTO & Co-founder SigmaXL, Inc.
www.SigmaXL.com
www.linkedin.com/in/johnnoguera

## Slide 2: Agenda
Fraction of Design Space (FDS) Plot
Summary: Interpreting the FDS Plot
Cake Bake RSM Example 1 (1 Replicate)
Cake Bake RSM Example 2 (2 Replicates)
Cake Bake FDS Overlay Plots
CCD Rotatable vs CCD Face Centered vs Box-Behnken

## Slide 3: Agenda
Optimal Designs: Comparison to Factorial Designs
Optimal Designs: Comparison to Central Composite RSM Designs
Summary: When to Use Optimal Designs
D-Optimal Designs
I-Optimal Designs
A-Optimal Designs
Fraction of Design Space (FDS) Plot
Optimal Design Diagnostic Metrics
Optimal Design SE/VIF Metrics
Summary: Selecting an Optimal Design Type

## Slide 4: Agenda
Constrained D-Optimal Design – Adhesive Bond Strength
Questions
FDS Formula Details
Optimal Design Diagnostic Metrics and Formulas
References

## Slide 5: Fraction of Design Space (FDS) Plot
Power analysis is very useful to assist in the design of 2-level factorial and fractional-factorial experiments. In a similar manner, the Fraction of Design Space (FDS) Plot assists the practitioner to select and right size their response surface and optimal designs.
The FDS Plot was introduced by Zahran, Anderson-Cook and Myers ‎[8].
The FDS Plot provides a visual representation of how well the design covers the experimental space and helps in assessing the precision of predictions that can be made from the design.

## Slide 6: Fraction of Design Space (FDS) Plot
This can be used to compare and select number of replicates, number of center points, Central Composite alpha axial value, Central Composite vs Box-Behnken and optimality criterion.
The FDS Plot will show Prediction Standard Error of the Mean (SE Mean) vs Fraction of Design Space and Margin of Error vs Fraction of Design Space.

## Slide 7: Fraction of Design Space (FDS) Plot
When comparing FDS Plots, lower is better and flatter is better over the majority of the design space.
The FDS Plot is produced prior to any data collection. Like the power calculations used in factorial designs, FDS assumes that the model standard deviation is 1.
If the standard deviation is known, multiply the FDS Plot values by this standard deviation to get actual response units.
If you know the process standard deviation you can use the Margin of Error plot to assess if the actual prediction error will be acceptable over the majority of the design space (typically use FDS = 80 to 95%).

## Slide 8: Fraction of Design Space (FDS) Plot
A model must be specified for FDS, typically that will be an RSM Quadratic model (Main Effects + 2-Way Interactions + Quadratic Terms) with 95% Confidence Level.
The FDS Plots are computed using Monte Carlo simulation with a uniform distribution and coded values from -1 to +1, hence cuboidal. This occurs even for rotatable Central Composite designs which allows for comparison of FDS Plots across various design types.
Formula details are given in the SigmaXL Workbook Appendix: Fraction of Design Space (FDS) Plots.

## Slide 9: Fraction of Design Space (FDS) Plot
SE Mean and Margin of Error are computed for 100,000 random values.
These are sorted from smallest to largest, and the results are plotted as SE Mean vs Fraction of Design Space and Margin of Error (Interval Half-Width) vs Fraction of Design Space using 1000 plot points.
Overlay FDS Plots will be used to compare the different design options.

## Slide 10: Summary: Interpreting the FDS Plot
SE Mean and Margin of Error – smaller is better, flatter is better, over the majority of the design space.
Try to achieve this with minimum runs.
If the process standard deviation is known, multiply the SE Mean and Margin of Error by the standard deviation to estimate the actual prediction error vs fraction of design space.

## Slide 11: Cake Bake RSM Example 1
This is the layer cake baking experiment revisited. The response variable is Taste Score (on a scale of 1-7 where 1 is "awful" and 7 is "delicious"). Average scores for a panel of tasters have been recorded. The X Factors are A: Bake Time (20 to 40 minutes) and B: Oven Temperature (350 to 400 F).
The experiment is a 10-Run, Central Composite Design (CCD) with 2 Center Points, Face Centered with Alpha Axial = 1.0.
We will first introduce the concept of the Fraction of Design Space Plot by analyzing this data and manually inputting values into the Predicted Response Calculator.

## Slide 12: Cake Bake RSM Example 1
Cake Bake RSM Example 1 was created by clicking: SigmaXL > Design of Experiments > Advanced Design of Experiments: Response Surface > Response Surface Designs.
Central Composite Design:
2 Center Points
Face Centered
1 Replicate
FDS Plot:
Quadratic Model
95% CI

## Slide 13: Cake Bake RSM Example 1
Open the file RSM FDS Example – Cake Bake.xlsx, Sheet Example 1.
Runs are randomized in the actual experiment, but standard order is used for this demonstration.

## Slide 14: Cake Bake RSM Example 1
SigmaXL > Design of Experiments > Advanced Design of Experiments: Response Surface > Analyze Response Surface Design

## Slide 15: Cake Bake RSM Example 1

## Slide 16: Cake Bake RSM Example 1
Scroll to the Predicted Response Calculator. Enter the center point values Time = 30 and Temp = 375. This gives a Predicted Response for Taste = 6.57 with a Standard Error = 0.15 and 95% CI = 6.15 to 6.99.
The Margin of Error (Interval Half-Width) is 6.99 – 6.57 = 0.42. This is a wide interval considering that the taste score is on a scale of 1 to 7.

## Slide 17: Cake Bake RSM Example 1
Now enter Time = 20 and Temp = 350. This gives a Predicted Response for Taste = 6.29 with a Standard Error = 0.22 and 95% CI = 5.66 to 6.91
The Margin of Error (Interval Half-Width) is 6.91 – 6.29 = 0.62. This is an even wider interval than that obtained with the center points.

## Slide 18: Cake Bake RSM Example 1
The Fraction of Design Space (FDS) Plot will repeat the above process 100,000 times using a uniform random number from 20 to 40 for Time and 350 to 400 for Temp. to obtain 100,000 SE and Half-Interval values.
These are sorted from smallest to largest and the results are plotted as SE Mean vs Fraction of Design Space and Margin of Error (Interval Half-Width) vs Fraction of Design Space using 1000 plot points.

## Slide 19: Cake Bake RSM Example 1
Hover the mouse cursor on the FDS plot to obtain values for any fraction of design space.
Smaller is better and flatter is better, over the majority of the design space.

## Slide 20: Cake Bake RSM Example 1
The FDS Summary Statistics complement the FDS Plot.
Looking at the 95th Percentile (i.e., 95% of the design space), we see that the SE Mean can be as large as .72 and the Margin of Error (Interval Half-Width) as large as 1.99.

## Slide 21: Cake Bake RSM Example 1
To obtain units of Taste Score, we multiply by the model standard deviation: SE Mean = 0.72*0.25 = 0.18 and Half-Width = 1.99*0.25 = 0.5.
As noted previously, this is a large margin of error considering that the taste score is on a 7-point scale.
Note that the Confidence Level of 95% applies to the Margin of Error. The 95th Percentile applies to the Fraction/Proportion of Design Space.
Since these percentiles are based on Monte Carlo simulation, slightly different results will be observed every time they are produced unless a fixed seed is used.

## Slide 22: Cake Bake RSM Example 2
Cake Bake RSM Example 2 was created by clicking: SigmaXL > Design of Experiments > Advanced Design of Experiments: Response Surface > Response Surface Designs.
Central Composite Design:
2 Center Points
Face Centered
2 Replicates, Block on Replicates
FDS Plot:
Quadratic Model, 95% CI
Include Blocks

## Slide 23: Cake Bake RSM Example 2
Open the file RSM FDS Example – Cake Bake.xlsx, Sheet Example 2.
This has 2 Replicates of the previous Cake Bake design, with Block on Replicates.
This will demonstrate the impact that replicates have on the SE Mean and Margin of Error (Interval Half-Width).

## Slide 24: Cake Bake RSM Example 2

## Slide 25: Cake Bake RSM Example 2
SigmaXL > Design of Experiments > Advanced Design of Experiments: Response Surface > Analyze Response Surface Design

## Slide 26: Cake Bake RSM Example 2

## Slide 27: Cake Bake RSM Example 2
Refit with Blocks removed.

## Slide 28: Cake Bake RSM Example 2
Scroll to the Predicted Response Calculator. Enter the center point values Time = 30 and Temp = 375. This gives a Predicted Response for Taste = 6.48 with a Standard Error = 0.08 and 95% CI = 6.31 to 6.66.
The Margin of Error (Interval Half-Width) is 6.66 – 6.48 = 0.18. This is a dramatic reduction from the previous value of 0.42 and is an acceptable interval for the 1-7 taste score.

## Slide 29: Cake Bake RSM Example 2
Hover the mouse cursor on the FDS plot to obtain values for any fraction of design space.
Smaller is better and flatter is better, over the majority of the design space.

## Slide 30: Cake Bake RSM Example 2
The FDS Summary Statistics complement the FDS Plot.
Looking at the 95th Percentile (i.e., 95% of the design space), we see that the SE Mean can be as large as .55 and the Margin of Error (Interval Half-Width) as large as 1.2.

## Slide 31: Cake Bake RSM Example 2
To obtain units of Taste Score, we multiply by the model standard deviation: SE Mean = 0.55*0.19 = 0.1 and Half-Width = 1.2*0.19 = 0.23.
As noted, this is an acceptable margin of error for the 1-7 taste score.
The FDS Plot for Example 2 included Blocks so could be redone without Blocks, but we will not do so here.

## Slide 32: Cake Bake FDS Overlay Plots
SigmaXL > Design of Experiments > Advanced Design of Experiments: Overlay FDS Plots

## Slide 33: Cake Bake FDS Overlay Plots
Here we can see a dramatic reduction in SE Mean and Margin of Error from the 2 Replicates vs 1 Replicate design!

## Slide 34: CCD Rotatable vs CCD Face Centered vs Box-Behnken
SigmaXL > Design of Experiments > Advanced Design of Experiments: Response Surface > Response Surface Designs
Central Composite Design (CCD) Rotatable:
Three Factors
16 Run
2 Center Points
Alpha = 1.682
1 Replicate
16 Run CCD is selected for comparison to 15 Run Box-Behnken

## Slide 35: CCD Rotatable vs CCD Face Centered vs Box-Behnken
SigmaXL > Design of Experiments > Advanced Design of Experiments: Response Surface > Response Surface Designs
Central Composite Design (CCD) Face Centered:
Three Factors
16 Run
2 Center Points
Alpha = 1
1 Replicate

## Slide 36: CCD Rotatable vs CCD Face Centered vs Box-Behnken
SigmaXL > Design of Experiments > Advanced Design of Experiments: Response Surface > Response Surface Designs
Box-Behnken Design:
Three Factors
15 Run
3 Center Points
1 Replicate

## Slide 37: CCD Rotatable vs CCD Face Centered vs Box-Behnken
Central Composite Design (CCD) Rotatable
Central Composite Design (CCD) Face Centered
Box-Behnken Design

## Slide 38: CCD Rotatable vs CCD Face Centered vs Box-Behnken
CCD Rotatable (CCD Rot) has the flattest FDS Plot, and the smallest SE Mean and Margin of Error in 40% of the design space. This design is recommended if five levels are possible.
CCD Face Centered (CCD Face) has the smallest SE Mean and Margin of Error in 60% of the design space.
Box-Behnken (BB) has the largest SE Mean and Margin of Error in 40% of the design space. This is due to not having points at the cube corners.

## Slide 39: Optimal Designs: Comparison to Factorial Designs
Factorial and Fractional Factorial Designs have ideal optimality statistics (Efficiency = 100% when there is no center point), are orthogonal, have a clearly defined alias structure, and are easy to understand.
Categorical Factors for Factorial Designs are limited to 2 levels; more levels are permitted with General Factorial Designs, but they quickly explode in number of runs.
Factorial Designs cannot accommodate factor constraints.
Optimal designs are more efficient than Factorial designs.

## Slide 40: Optimal Designs: Comparison to Central Composite RSM Designs
Central Composite Response Surface designs are typically rotatable (i.e., have the same prediction variance at all points that are the same distance/radius from the center of the design, regardless of direction), with Uniform Precision (nearly flat FDS) and close to I-Optimal.
Categorical Factors are permitted but the RSM design is replicated for each level combination, so quickly explodes in number of runs.
RSM designs cannot accommodate factor constraints.
Optimal designs are more efficient than RSM designs.

## Slide 41: Summary: When to Use Optimal Designs
There are linear factor constraints.
You have a mix of continuous and multi-level categorical factors.
Runs are expensive or difficult, so you need the most efficient design possible.
The model to be used is not a straightforward main effects + 2-way interaction + quadratic model. For example, you might want to estimate a quadratic term only for specific factors or to estimate cubic terms.
Augment an existing design (coming in V11.1).

## Slide 42: D-Optimal Designs
A D-Optimal design maximizes the determinant of the information matrix, which minimizes the volume of the joint confidence region of the estimated regression coefficients.
This results in good overall model precision, so is recommended as a general-purpose alternative to screening and two-level factorial designs.

## Slide 43: D-Optimal Designs
Joint confidence ellipsoids (95% confidence) for two regression parameters (and ) under two different experimental designs. The D-optimal design (blue ellipse) leads to a much smaller ellipse (lower joint uncertainty) than a suboptimal design (red ellipse) that has a lower . In higher dimensions, D-optimality analogously minimizes the hyper-volume of the confidence ellipsoid for all parameters.
This property makes D-optimal designs especially useful when we care about the overall precision of all model coefficients together, rather than any single coefficient in isolation.

## Slide 44: D-Optimal Designs
Example: 2 Factor, D-Optimal design with a Main Effects + 2-Way Interactions + Quadratic model, with 6 additional runs for model, giving a Total No. of Runs = 12.
From this chart of factor settings for A, B, we can see that the D-Optimal design has selected a 3-level full-factorial and added replicates in the corners.

## Slide 45: I-Optimal Designs
An I-Optimal design minimizes the trace of , where is the moment matrix for the given model.
This minimizes the average prediction variance (integrated variance) over the design space, which can be thought of as minimizing the area under the Fraction of Design Space (FDS) Plot.
Since the primary objective of a Response Surface design is accurate prediction and optimization, I-Optimality is recommended for RSM designs.
For details on the moment matrix, see the Goos and Jones ‎book [1].

## Slide 46: I-Optimal Designs
Example: 2 Factor, D-Optimal design with a Main Effects + 2-Way Interactions + Quadratic model, with 6 additional runs for model, giving a Total No. of Runs = 12.
From this chart of factor settings for A, B, we can see that the I-Optimal design has also selected a 3-level full-factorial and added replicates to the center points.

## Slide 47: A-Optimal Designs
An A-Optimal design minimizes the trace of (the trace of the inverse of the information matrix), which minimizes the average variance of the estimated regression coefficient terms and is recommended for screening designs by Jones. et. al.[2].
The A-optimality criterion is more consistent with the screening objective than the D-optimality criterion. The goal of screening experiments is to identify an active subset of the factors. An A-optimal design minimizes the average variance of the parameter estimates, which is directly related to that goal.

## Slide 48: A-Optimal Designs
While there are many cases where A- and D-optimal designs coincide, the A-optimal designs tend to have better statistical properties when the A- and D-optimal designs differ. In such cases, A-optimal designs generally have more uncorrelated columns in their model matrices than D-optimal designs.
A-optimal designs can also substantially reduce the worst prediction variance compared to D-optimal designs.

## Slide 49: A-Optimal Designs
Example: 2 Factor, A-Optimal design with a Main Effects + 2-Way Interactions + Quadratic model, with 6 additional runs for model, giving a Total No. of Runs = 12.
From this chart of factor settings for A, B, we can see that the A-Optimal design has also selected a 3-level full-factorial and added replicates to the center points and an edge point.

## Slide 50: Fraction of Design Space (FDS) Plot
As expected, I-Optimal has the lowest overall SE Mean and Margin of Error since its optimality criterion minimizes average prediction error, but only slightly, and A-Optimal is approximately the same as I-Optimal for 50% of the design space.
D-Optimal has the largest SE Mean and Margin of Error except for a small percent of the design space (at the corners).

## Slide 51: Optimal Design Diagnostic Metrics
Metric | Goal
D-Optimality** (Determinant of X'X) | Max**
D-Efficiency | 100
Determinant of Inv(X'X) | Min
A-Optimality (Trace of Inv(X'X)) | Min
A-Efficiency | 100
Max Prediction Variance | Min
G-Efficiency | 100
I-Optimality (Avg Prediction Variance) | Min
Condition Number | 1
The double asterisks ** denotes the metric that is used as the objective function. The goal is given as Max, Min or numeric value.

## Slide 52: Optimal Design Diagnostic Metrics
The D, A and G-Efficiency metrics compare the efficiency of the design to that of an ideal orthogonal design in terms of the respective optimality criterion.
A full or fractional factorial design (without center points) would have D-Efficiency, A-Efficiency and G-Efficiency all equal to 100%.
The efficiency metrics are easier to interpret than the optimality metrics since they are scaled from 0 to 100, but note that for D and A-Efficiency, we do not have “rules of thumb” to aid in interpretation. These efficiency metrics should be used as indicators to compare designs that have the same number of runs ‎[1].

## Slide 53: Optimal Design Diagnostic Metrics
Max Prediction Variance and G-Efficiency are calculated using Monte Carlo sampling of the design space as done in the Fraction of Design Space (FDS) Plot with 1e6 replicates. Therefore, calculations for the same design might vary slightly.
Montgomery et al. ‎[4] note: “Usually a G-Efficiency of around 50% or higher is desired. Standard response surface designs in regularly shaped regions typically have G-Efficiencies well above 50%, and often they are in the 70–90% range.”

## Slide 54: Optimal Design Diagnostic Metrics
Montgomery et al. ‎[5] give a rule of thumb for condition number: > 100 indicates moderate multicollinearity.
Model term SE, VIF and TOL are also reported. These are the same values that would be obtained in a regression model with error standard deviation = 1.

## Slide 55: Optimal Design Diagnostic Metrics
Optimal Design Diagnostic Metrics for the previous 2 Factor, 12 Run designs with a Main Effects + 2-Way Interactions + Quadratic model.
As expected, the Efficiency scores are highest for their respective optimality criterion. However, A-Optimality has the highest G Efficiency (i.e., lowest maximum variance), lowest Condition Number, approximately the same Avg Prediction Variance as I-Optimality, and a higher D Efficiency than the I-Optimal design.

## Slide 56: Optimal Design SE/VIF Metrics
Optimal Design SE/VIF Metrics for the previous 2 Factor, 12 Run designs with a Main Effects + 2-Way Interactions + Quadratic model.
Note, RMSE has been added using the formula =SQRT(SUMSQ(C43:C47)/5). Max VIF is also shown.
As expected, A-Optimal has the lowest RMSE for the Model Terms. It also has the lowest Max VIF score.

## Slide 57: Summary: Selecting an Optimal Design Type
In this example, with 12 runs and quadratic model, the best overall design choice is A-Optimal, but one cannot conclude that A-Optimal is generally preferred for a two factor RSM design, one would need to compare and evaluate for each design case.
A-Optimal minimizes the average variance of the estimated regression coefficient terms and is recommended for screening designs.

## Slide 58: Summary: Selecting an Optimal Design Type
Since the primary objective of a Response Surface design is accurate prediction and optimization, I-Optimality is generally recommended for RSM designs.
D-Optimal, with its good overall model precision, is recommended as a general-purpose alternative to screening and two-level factorial designs.
The Optimal Design Metrics, SE, VIF, TOL and FDS Plots are all produced prior to any data being collected so design evaluation and selection can easily be done beforehand.

## Slide 59: Constrained D-Optimal Design – Adhesive Bond Strength
This example demonstrates the use of a D-Optimal design with constraints, as given in the paper by Montgomery D.C. et al. (2002) “Experimental Designs for Constrained Regions”, Quality Engineering, 14(4), pp. 587–601 [4].
“An experimenter is investigating the bond strength of a particular adhesive. The adhesive is applied to two parts and then the assembly cured at an elevated temperature. The two factors of interest are the amount of adhesive applied (A) and the cure temperature (B). Over the ranges of these factors, taken from -1 to 1 on the usual coded design variable scale, the experimenter knows that if too little adhesive is applied and the cure temperature is too low, the parts will not bond satisfactorily… Furthermore, if the temperature is too high and too much adhesive is applied, either the parts will be damaged by stress or an inadequate bond will result.”
The linear constraint formulas are given as:
A+B >= -0.5
A+B <= 1
The expected range of bond strength values is approximately 1 to 4. For demonstration purposes we will assume a process historical standard deviation = 0.1.

## Slide 60: Constrained D-Optimal Design – Adhesive Bond Strength

## Slide 61: Constrained D-Optimal Design – Adhesive Bond Strength
Note that with a constrained design, the continuous factors can take on any value between -1 and 1 (or low to high) and are displayed to 3 decimal places. The constraints can be checked by summing the two factor columns row-wise and by creating an Excel Scatter Chart of the factor settings.

## Slide 62: Constrained D-Optimal Design – Adhesive Bond Strength
Notice that the constraints effectively remove two corners of the original square region of operability, and this results in an irregular experimental region. We can see that the constraint formulas have been met and that there are two replicates in the center of the constrained region, and at (0,1), (1,0), and (1,-1). Note that the center of the constrained region is not the same as (0,0) center points.

## Slide 63: Constrained D-Optimal Design – Adhesive Bond Strength
The D-Efficiency and A-Efficiency values are low, but they cannot be used as a measure of design quality standalone, they are used for comparison to other designs. On the other hand, we see that the G-Efficiency is good and is greater than 50% as recommended by Montgomery. The condition number = 56.4 is high, but still less than Montgomery’s rule of thumb where > 100 is moderate. The maximum VIF score is 11.8 which is higher than the recommended maximum of 5, but this degree of multicollinearity is an unavoidable consequence of adding constraints to the design.

## Slide 64: Constrained D-Optimal Design – Adhesive Bond Strength
Looking at the 95th Percentile (i.e., 95% of the design space), we see that the SE Mean can be as large as 0.68 and the Margin of Error (Interval Half-Width) as large as 1.78. To obtain units of Bond Strength, we multiply by the process historical standard deviation: SE Mean = 0.68*0.1 = 0.068 and Half-Width = 1.78*0.1 = 0.178. This is an acceptable margin of error for the bond strength which has an expected range of values of 1 to 4.
Note that the Confidence Level of 95% applies to the Margin of Error. The 95th Percentile applies to the Fraction/Proportion of Design Space.

## Slide 65: Constrained D-Optimal Design – Adhesive Bond Strength
Open file Montgomery Adhesive Bond Strength.xlsx. This has the design worksheet populated with Bond Strength values.

## Slide 66: Constrained D-Optimal Design – Adhesive Bond Strength
SigmaXL > Design of Experiments > Advanced Design of Experiments: Optimal > Analyze Optimal Design

## Slide 67: Constrained D-Optimal Design – Adhesive Bond Strength
There is no significant Lack of Fit, all model terms are significant, and the R-Square, R-Square Adjusted and R-Square Predicted are very high. Note that the VIF and Tolerance values match those given in the design report, with the maximum VIF = 11.8 due to the design constraints. The Predictor Term SE Coefficient values divided by S match those given in the design report.

## Slide 68: Constrained D-Optimal Design – Adhesive Bond Strength
The residuals look good with no obvious non-normality or patterns.

## Slide 69: Constrained D-Optimal Design – Adhesive Bond Strength
The Margin of Error (Interval Half-Width) is 1.006 – 0.862 = 0.144, which is close to what we estimated using the FDS Plot. Given that the Strength range of values is approximately 1 to 4, this is an acceptable margin of error for prediction.
Note that the Predicted Response Calculator allows settings that are outside of the constraint region, in which case the predicted response would be an extrapolation.

## Slide 70: Constrained D-Optimal Design – Adhesive Bond Strength
Adhesive = 1 and Temp = 0 give maximum Bond Strength. This agrees with the maximum settings given in the paper, although other maximum values are also possible.

## Slide 71
Questions?
What’s New in SigmaXL® Version 11 Part 3 of 3: Evaluating Response Surface Designs with the Fraction of Design Space (FDS) Plot and Introduction to Optimal Designs July 30, 2025

## Slide 72: FDS Formula Details
The prediction variance at each of the Monte-Carlo replicated design points in the design space is given by:
where is the variance of the error term, and assumed to be equal to 1, and is the design matrix, after mapping by the specified model. Note, the FDS design space is always cuboidal, even if the original design is rotatable/spherical. This allows for comparison across various design types.
The Monte Carlo sample size is 100,000 with a uniform distribution having values from low to high (coded -1 to +1) for each continuous factor and integer distribution (coded -1/0/1) for each categorical factor and blocking variable. If linear constraints are specified for continuous factors in an Optimal design, only values that satisfy the constraint formula(s) are used. The starting sample size is 200,000 and the final sample size is reported.

## Slide 73: FDS Formula Details
The standard error of prediction at a point is the square root of the prediction variance:
The margin-of-error (interval half-width) is given by:
where is the inverse of the Student’s t CDF, is the degrees of freedom in the design matrix, and is the alpha risk.

## Slide 74: Optimal Design Diagnostic Metrics and Formulas

## Slide 75: References
Goos, P., and Jones, B. (2011). Optimal design of experiments: A case study approach, John Wiley & Sons.
Jones, B., Allen-Moyer, K., and Goos, P. (2021). “A-optimal versus D-optimal design of screening experiments”, Journal of Quality Technology, 53(4), pp. 369–382.
Montgomery, D. C. (2020). Design and Analysis of Experiments, 10th Edition, John Wiley & Sons.
Montgomery, D. C., Loredo, E. N., Jearkpaporn, D., and Testik, M. C. (2002). “Experimental Designs for Constrained Regions.” Quality Engineering, 14(4), pp. 587–601.
Montgomery, D. C., Peck, E.A. and Vining, G.G. (2021). Introduction to Linear Regression Analysis, 6th Edition, John Wiley & Sons.
Myers, R. H., Montgomery, D. C., Anderson-Cook, C. M. (2016). Response Surface Methodology: Process and Product Optimization Using Designed Experiments, Fourth Edition, John Wiley & Sons.

## Slide 76: References
Walsh, S. J., Lu, L. and Anderson-Cook, C. M. (2023). “I-optimal or G-optimal: Do we have to choose?”, Quality Engineering, 36(2), pp. 227–248.
Zahran, A., Anderson-Cook, C. M. and Myers, R. H. (2003). “Fraction of Design Space to Assess Prediction Capability of Response Surface Designs”, Journal of Quality Technology, 35(4), pp. 377–386.